## Slide 1
A Research Roadmap for Physical AI Systems
Arnab Raha
Chief NPU Architect
Intel AI
IBM IEEE CAS/EDS – AI Compute Symposium – October 2026

## Slide 2: Robotics is Entering the Physical AI Era
Robotics Compute Architectures Must Evolve
Traditional Robotics
Fixed programming
Rule-based control
Dedicated controllers
Predictable workloads
Physical AI Robotics
VLMs
VLA Models
Diffusion Policies
Imitation Learning
Autonomous Planning
New Challenge
Robots must:
✅ Reason ✅ Perceive ✅ Plan ✅ Act ✅ Stabilize
All simultaneously
Notes: Key Message: Physical AI requires a fundamentally new compute architecture.

## Slide 3: The Opportunity
Physical AI Market Inflection Point
Requirements
2000 TOPs
16 Cameras
256 GB Memory
<100 ms Vision to Action

## Slide 4
Why Current AI SoCs Are Not Enough
Monolithic NPU Architecture
Single Large NPU
Planning
Perception
VLA
Safety
Control
All workloads compete for:
Compute
Memory
Fabric
Scheduling
Result:
❌ Latency Variance
❌ Resource Contention
❌ Safety Challenges
❌ Scalability Limits

## Slide 5
The Robotics Brain Architecture
Key Observation
  These workloads are fundamentally different
  A single NPU cannot optimize all three simultaneously

## Slide 6
Why Multi-NPU?
Physical AI introduces three simultaneous execution domains:
System 0 : Real-Time Control (~1 kHz)
System 1 : Action Generation (10-200 Hz)
System 2 : Reasoning (1-7 Hz)
Monolithic NPUs are not optimized for all three.
Multi-NPU is not about achieving higher TOPs
It is about isolating cognitive functions operating at different timescales, safety domains, and resource requirements.

## Slide 7
Introducing Multi-NPU Architecture
Each NPU optimized for a specific cognitive task.
  Benefits
  ✅ Isolation
  ✅ Deterministic Execution
  ✅ Better Scaling
  ✅ Improved Safety
  ✅ Higher Utilization

## Slide 8
Multi-NPU Solves Compute Scaling
Traditional Scaling : One Giant NPU
Problems
Bigger die
Higher cost
Yield loss
Power inefficiency
Benefits
✅ Modular growth
✅ Better yield with Tiled/Chiplet based
✅ Product segmentation
✅ Future scaling to 3000+ TOPs
Multi-NPU Scaling : N instances of NPUs x M TOPs per NPU instance
Challenge #1  2000 TOPs Requirement

## Slide 9
Multi-NPU Solves Memory Bandwidth
Monolithic Architecture : Shared DRAM
Results:
Contention
Cache thrashing
Latency spikes
Benefits:
✅ Distributed bandwidth
✅ Lower latency
✅ Localized data processing
✅ Better efficiency
Multi-NPU Memory Hierarchy
Challenge #2  1 TB/s Bandwidth

## Slide 10
Multi-NPU Solves Vision-to-Action Latency
Current Pipeline : Sequential Execution
Results:
Latency accumulation
AI tasks block control decisions
Resource contention
Poor scalability
Jitter and Unpredictability
Benefits:
✅ Reduced latency
✅ Higher throughput
✅ Concurrent execution
Multi-NPU Pipeline : Parallel Execution
Challenge #3  <100 ms Response

## Slide 11
Multi-NPU Solves Real-Time Determinism
Current Risk
Potential Instability:
VLM Spike
Memory Congestion
Control Misses Deadline
Benefits:
✅ Hard real-time operation
✅ Bounded latency
✅ No AI interference
Dedicated Real-Time NPU :
System 0 NPU (Reserved Resources, Reserved Bandwidth and Reserved Memory)
Challenge #4  1 kHz Control Loop

## Slide 12
Multi-NPU Solves Functional Safety
Traditional Architecture :
Problems:
Safety shares resources with AI
Single point of failure
Safety Island NPU
Functions:
Emergency stop
Torque limits
Action validation
Human proximity monitoring
Benefits :
✅ Independent power
✅ Protected memory
✅ Secure boot
✅ Lockstep execution
Challenge #5 – Safe Physical Actions

## Slide 13
Multi-NPU Solves Camera Scaling
Future Humanoid
16 Cameras
Force Sensors
Audio
Tactile Sensors
Benefits:
✅ Linear camera scaling
✅ Reduced memory traffic
✅ Lower latency
Distributed Sensor Fabric
Challenge #6  16 Camera Robotics

## Slide 14
Monolithic NPU Vs Multi-NPU

## Slide 15
Hardware Architecture
Key HW Features
4-16 NPUs
Unified Address Space
QoS Aware Fabric
TSN Support
16 Camera Support
Functional Safety
Robotics Multi-NPU SoC

## Slide 16
The Fabric Is the Computer
Today’s Focus
More NPUs
More TOPs
More Models
Tomorrow’s Bottleneck :
Moving Data
Synchronizing State
Sharing Context
Meeting Deadlines
Inter-NPU Communication Will Define Multi-NPU Scalability

## Slide 17
Multi-NPU Creates New Challenges
New Challenges
  ⚠ Fabric bandwidth
  ⚠ Synchronization
  ⚠ Data locality
  ⚠ Memory coherence
  ⚠ Distributed scheduling
  ⚠ Runtime complexity
  ⚠ Software fragmentation
Benefits
  ✅ Specialization
  ✅ Isolation
  ✅ Modularity
  ✅ Scalability
Multi-NPU is not a free scaling mechanism. It shifts the challenge from computation to communication, orchestration, and memory management.

## Slide 18
Software Architecture
Key SW Features
Model Placement
NPU Scheduling
Resource Management
Safety Enforcement
Robotics Distributed Runtime
Software Stack : OpenVINO + ROS 2 + Real-Time Linux + oneAPI

## Slide 19
Software Architecture : Layer 1
Functions
Model Optimization
  Converts (PyTorch, TensorFlow, JAX, ONNX) into optimized execution graph
Model Quantization
  Supports FP32, FP16, INT8, INT4, FP4
Hardware Abstraction
  Developer writes : deploy (model)
  OpenVINO decides :
    CPU
    GPU
    Planner NPU
    VLA NPU
    RT NPU
OpenVINO : The AI deployment framework for Robotics

## Slide 20
Software Architecture : Layer 2
Responsibilities
Device Management
  Sensors (Cameras, Lidar, IMU, Force sensors)
Robotics Services
  Mapping
  Localization
  Motion Planning
  State estimation
Communication
  DDS Middleware
  Publisher/Subscriber Architecture
ROS 2 : The application framework of robotics

## Slide 21
Software Architecture : Layer 3
Role : Provides the 1 kHz+ Control Loop Support
Deterministic Scheduling
  Guarantee execution windows
Resource Isolation
  Provides Control NPU from Planner NPU activities
Low Latency Interrupts
  Critical for :
    Motor control
    Sensors
    Functional Safety
Real-Time Linux : Guarantees deterministic behavior

## Slide 22
Software Architecture : Layer 4
Functions
Cognitive Domain APIs
  Reasoning Task
  Policy Task
  Control Task
  Safety Task
Multi-NPU Placement
  Queues for Planner, Action and Real-Time tasks
Unified Memory
  Developer sees single pointer
  Runtime handles behind the scenes
    HBM
    LPDDR
    SRAM
Robotics-Specific oneAPI Extensions